## Slide 1: Modular R.O.V for Sub-Sea Operations
Oluyemi Farayibi
Juan Gomez
Gustav Guijt
David Martinez
Victor Ortiz
Olly
Project Update 1
10/19/2015

## Slide 2: Safety Moment: Do you even lift bro?
Olly

## Slide 3: ROV Presentation Outline
Project Objectives / Timeline
2016 MATE Competition
MATE Competition Specs
Design Overview
First Frame Design
Second Frame Design
Stress Analysis – Frame 1
Stress Analysis – Frame 2
Control System
Propulsion System
Thruster Positioning
Arm Update
Updated Project Budget
Olly

## Slide 4: Team Objective
  Team HydroBurst’s primary objective is to design, test, and construct an underwater remotely operated vehicle (ROV) to compete in the 2016 National and International MATE Competitions.
Olly

## Slide 5: 2016 MATE Competition
Outer Space: Mission Europa
  Measure thickness of ice
  Measure total depth
  Measure temp of thermal vents
  Retrieve and connect ESP cable
David

## Slide 6: 2016 MATE Competition
Inner Space: Mission-critical equipment recovery
  Survey the seafloor
  Collect equipment located on sea floor
Inner Space: Forensic Fingerprinting
  Collect oil sample
  Analyze a gas chromatograph
David

## Slide 7: 2016 MATE Competition
Inner Space: Deepwater Coral Study
  Photograph corals and compare with last years images
  Collect coral samples for analysis
Inner Space: Rigs to reefs
  Attach a flange to top of wellhead
  Secure flange with two bolts
  Install cap on flange
  Secure the cap with four bolts
David

## Slide 8: MATE Competition Specs
Size Constraints (released September 30th):
  Maximum Diameter of 85cm
    +5 Points for diameter between 64.1cm and 70cm
    +10 points for diameter between 58.1cm and 64cm
    +20 points for diameter less than 58cm
  Mass
    +5 Points for mass between 19.01kg and 22kg
    +10 points for mass between 17.01kg and 19kg
    +20 points for mass less than 17kg
Our Design Goals based on Constraints:
  Diameter less than 58cm (22.8346 inches).
  Mass less than 17kg (37.4786 lbf)
Gustav

## Slide 9: Design Overview
As covered during the last presentation:
  we weighed the pros and cons of various standard ROV frame designs.
  Decided upon the Octagonal model as the most effective model.
 | Maneuverability | Hydro-dynamics | Internal Space Utilization | Modular Optimization | Corrosion Resistance | Totals
Rectangular | 1 | 1 | 2 | 3 | 5 | 12
Cylindrical | 3 | 4 | 3 | 1 | 5 | 16
Octagonal | 4 | 3 | 2 | 3 | 5 | 17
Flat | 2 | 3 | 3 | 2 | 5 | 16
Gustav

## Slide 10: First Frame Design
Shape: Rhombicuboctahedron
  To make it as spherical as possible using existing fittings.
Material: CPVC
  Light weight, designed for water usage, and can handle high pressures.
Maximum diameter: 21 inches
  Minimum of 1.00 inch clearance on all sides.
Frame weight: 4.5 lbs.
Complete Frame Assembly
Module (Arms, Sensors, etc…)
Gustav

## Slide 11: Second Frame Design
Shape: Octagonal Prism.
  Solid Frame.
Material: Plastic or Acrylic.
  Light weight and strong.
Maximum diameter: 21 inches.
  Minimum of 1.00 inch clearance on all sides.
Clear Dome on the front for access and Camera.
Gustav

## Slide 12: Stress Analysis – Frame 1
Quarter Frame
Full Frame
Juan

## Slide 13: Stress Analysis – Frame 1
Constraints
CPVC Material Definition
Juan

## Slide 14: Stress Analysis – Frame 1
Pressure
CPVC Material Assignment
Juan

## Slide 15: Stress Analysis – Frame 1 40 ft. below water
Displacement (in)
Von Mises Stress (psi)
Juan

## Slide 16: Stress Analysis – Frame 1 40 ft. below water
Displacement (in)
Von Mises Stress (psi)
Juan

## Slide 17: Stress Analysis – Frame 1 100 ft. below water
Displacement (in)
Von Mises Stress (psi)
Juan

## Slide 18: Stress Analysis – Frame 1
Model | Max. Von Mises Stress |  | Max. Displacement | 
 | 40 ft. depth | 100 ft. depth | 40 ft. depth | 100 ft. depth
Quarter Frame | 3296 psi | 9914 psi | 0.029 inches | 0.0734 inches
Full Frame | 3053 psi | 7633 psi | 0.045 inches | 0.112 inches
CPVC Material Properties:
  Tensile Strength (Yield Strength) 7,600 psi
  Allowable Stress = ⅔ σy 5066.67 psi
Juan

## Slide 19: Stress Analysis – Frame 2
Juan
ROV Frame
Acrylic Material Definition

## Slide 20: Stress Analysis – Frame 2
Displacement (in)
Von Mises Stress (psi)
Juan

## Slide 21: Control System
Feedback Sensors:
  Accelerometer.
  Gyroscope.
  3-in-1 Sensor: 9 Degrees of Freedom IMU (S24.95)
    3-axis accelerometer
    3-axis gyroscope
    3-acis magnetometer
David

## Slide 22: Control System
Communications:
  UART.
  I2C
  USB Hub
David

## Slide 23: Propulsion System
Blue Robotics T100 Thruster
  Price- $134.00 ea.
  Motor Type- High efficiency brushless
  Weight in air- 0.93 lb.
  Max Power- 130W
  Operating Voltage- 12 volts
  Max Thrust 5.2:4 Forward (5.2 lbf) Reverse (4 lbf)
  Min Thrust (0.03 lbf)
Olly

## Slide 24: Thruster Positioning
Olly

## Slide 25: Arms Update
Fast
High Torque
Accurate Rotation With Limited Angle (≈180°)
More complicated setup with PWM turning
Slow
Precise Rotation
Requires External Control Circuit or Microcontroller
Easy Set-Up & Control
Victor
Servo Motor
Stepper Motor
Servo Motors vs. Stepper Motors

## Slide 26: Arms Update
Victor

## Slide 27: Arms Update
Victor

## Slide 28: Updated Project Budget
Current Cash Flow:
  Expenditures:
    CPVC components ($86.35)
  Income:
    No Sponsors as of 10/19
Planned Expenditures:
  Final Frame - $100
  Propulsion System - $800
  Control System - $200
  Arm Module - $700
  Tether System - $200
  Total - $2,000
Victor

## Slide 29: Updated Gantt Chart
Gustav

## Slide 30: Thank You for Listening!
Any Questions, Comments, or Concerns?